Contact Map
# Introduction
Here we discuss the question: Is there an agent with the given bound or internal state?
# Definitions
The Contact Map is the map that contains a single agent copy of each type and shows all connections and internal states of the sites which can be produced in the simulation process. The LinkState of the site on this map can contain more than one LinkedSite.

The syntactic contact map takes into account any rule (dead or not) and
initial conditions (we summarize any bond that occurs in the lhs of a
rule, in the rhs of a rule, or in an initial species).

The semantic contact map is defined the same way, but only the rules which
are alive (or more precisely which are not proved dead) are taken into
account.
# Input Data
The Kappa model is the file with the system model with the set of Rules. This system model represents the initial system condition.
# Goal
Our goal is to build the ContactMap using the input data.
# Solution
The idea is to build the SubViews using the input data and fill in the map with the various Contact Map connections.
# Algorithm
1. Build the SubViews
2. Fill in the ContactMap:
  1. Initialize the ContactMap (create one sample for each agent type)
  2. For each SubView from SubViews add information about linkStates and InternalStates of all agents in the SubView to the ContactMap

# Examples

'1' A(x~u), B(x) -> A(x~u!1), B(x!1) @1.0
'2' A(x~p), C(x) -> A(x~p!1), C(x!1) @1.0

%init: 1*(A(x~u))
%init: 1*(B(x))
%init: 1*(A(x~p))
%init: 1*(C(x))

The step-by-step process description:

Retrieve the SubViews for this particular model:
Agent: A
- A(x~u)
- A(x~p)
- A(x~u!B.x)
- A(x~p!C.x)
Agent: B
- B(x)
- B(x!A.x)
Agent: C
- C(x)
- C(x!A.x)
Fill in the Contact Map according to the SubViews data:
Site A.x is grey. It means that it can have different Internal States.