Influence map
# Introduction
The Static Analysis is used in order to decide whether a model is wrong due to incorrect biological hypothesis or due to faulty action mechanisms. The Static Analysis relies on the species computation that can be produced during any execution. With such a tool it becomes
possible to specify some properties of a model before even trying to simulate it.

We try to understand causal dependences basing on the rules grammar. However, this dependence does not give us any quantitative characteristics.
# Definitions
The Influence map is an integration of the Activation map and the Inhibition map.

The Activation/Inhibition map is a digraph G: = (V,A), where
- V is the set of rules (vertices).
- A is the set of ordered couples of different vertexes (edges).
The Edge is the ordered couple of vertexes (v, w) where v is the beginning, and w is the end of an edge.
The edge (v, w) on the Activation Map shows that the rule v applying process has the positive influence on the rule w activity.
The edge (v, w) on the Inhibition Map shows that the rule v applying process has the negative influence on the rule w activity.
The Positive Influence means that after the rule v application a substance in Solution that is necessary for the rule w can appear.
The Negative Influence means that after the rule v application a substance in Solution that is necessary for the rule w can disappear.

Jerome said :
In the current state of the implementation, the computation of the
influence map in Complx is purely syntactic.
(We do not take into account reachables,views, and so on).

There is a positive edge between two rules r1 -> r2, if r1 modifies a bit
of information (called quark) that is tested in r2.

For instance:
r1: A(x~u) -> A(x~p)
r2: A(x~p) -> A(x~q)
r3: A(x~p!_) -> A(x~r!_)

Complx will report r1 -> r2
(r1: the site x of A take the internal state p,
  r2: check that the site x of A has the internal state p)
but also r1 -> r3 (for the same raison), even if there is no pushout
(A(x~p) is not compatible with A(x~p!_)).
The same way, there is a negative edge between two rules r1 -> r2, if r1
modifies a bit of information the former value of which was tested by r2.
r2 -|-> r3.

WARNING: the notion of modification is contextual. Potential side effects
have to be safely overapproximated thanks to the syntactic contact map.
Simplx may refine this influence map (by checking the existence of
pushouts, Jean is more informed than me on this point)

# Input Data
The Kappa model is the file with the system model with the set of Rules. This system model represents the Initial Solution.
# Goal
Our goal is to build the InfluenceMap using the input data.
# Solution
The idea of the solution is to generate the Contact Map and consider all the rules, rules influence on the ContactMap, as well as the other rules based on it. This will automatically fill out the InfulenceMap.
# Algorithm
Let us suppose that each site contains the information about agent's type that it belongs to.

for (rule : Rules)
1. Form the sites' lists (activatedSites), (inhibitedSites) that belong to these rules. While you add the site to any list, the site is marked according to the action that uses this site: BOUND, BREAK, etc:
  1. If the rule contains only the BREAK action for this site, and this site LinkState is SEMI_LINK or BOUND_OR_FREE, then we can find all the sites (findSites) that are connected to the site on the ContactMap. Add findSite to activatedSites, make LinkState FREE. Add findSite to the inhibitedSites; no alterations are made to the LinkState.
  2. If rule contains the DELETE action for the particular agent (agent of type A), then we can find all the sites (findSites) that can be connected with the agent of type A (excluding the connections presented in agent) using ContactMap. Add findSite to activatedSites, make LinkState FREE. Add findSite to the inhibitedSites; no alterations are made to the LinkState.
  3. If the site from the rule .leftHandSide participates in any action, then we add it to the inhibitedSites.
  4. We add all the sites with the rule .rightHandSide that are changed by this rule to the activatedSites . If the same site participates in more than one action related to the LinkState (for example, ADD, BOUND), then we add the site with the latest action only.
2. For (ruleCheck : Rules)
  1. Let the site a belong to the inhibitedSites that is marked with BOUND, BREAK, ADD, or DELETE action, and the site b belong to the ruleCheck.leftHandSide. Here a and b belong to the agents of the same type, then the site a type equals the site b type. Their LinkStates are the same, so we add the edge (rule, ruleCheck) to the Inhibition Map.
  2. Find the intersection of inhibitedSites and ruleCheck.leftHandSide (according to the InternalState) that is marked with the MODIFY action, by analogy. Add the edge (rule, ruleCheck) to the Inhibition Map.
  3. Find the intersection of activatedSites and ruleCheck.leftHandSide (according to the LinkState and InternalState), by analogy. Add the edge (rule, ruleCheck) to the Activation Map.

    A
    x

    activatedSites

    A
    x

    p

    A
    x

    u
    rule

    intersection

# Examples
'BND' A(x),B(y) -> A(x!1),B(y!1) @ 1.0
'BRK' A(x~p!1),B(y!1) -> A(x~p),B(y) @ 1.0
'MOD' A(x~p!_) -> A(x~u!_) @ 1.0

(*)	(**)
(***)
The green arrows show the Activation Map, the red ones show the Inhibition Map.

Let us analyze (*):
The BRK rule breaks the connection that leads to the A(x~p),B(y) agents formation. The new agents help to build new injections to the solution with the BND rule. It allows to apply this rule in the future as well. In other words, the BRK rule has the positive influence on the BND rule.
The BRK rule has the negative influence on the MOD rule because MOD is tested in the A(x~p!_) connection presence, and BRK usually breaks this connection.
The MOD rule has the negative influence on the BRK rule due to the Internal State alteration in, and BRK rule tests the A(x~p!1),B(y!1).

We can analyze (**), (***) in the similar way.
# Flowchart

start
rule : Rules

activatedSites, inhibitedSites = filingSites(rule)

ruleCheck : Rules

end
isIntersection(activatedSites, ruleCheck.leftHandSide)

Add (rule, ruleCheck) to the Activation Map

+
isIntersection(inhibitedSites, ruleCheck.leftHandSide)
Add (rule, ruleCheck) to the Inhibition Map

+