Dictionary
Here we explain the main concepts that are used for the project.

An Agent can contain one or several Sites. Each Site has the internal state and the link state (see the picture).

On the picture the agent A has two sites: y and x. The site y has the internal state u, the other sites have no internal state. The site y has the "Agent B site t" link state, the site t has the "Agent A site y" link state. The site x has the semi link link state; it means that the site is linked with some other site which is unimportant. The site z has the wild-card link state; it means that link state is unimportant at all. The site r has the free link state.

We can describe the picture in the symbolic form as A(y~u!1,x!_),B(t!1,r,z?).

The Rule consists of two collections of agents and the arrow between them. For example, A(x) → A(x!1),B(x!1),C(). Here the agent C has no sites.

The Solution is a collection of agents. We can apply rules to solution.

The Injection from the rule R to the solution S is a compatible bijection between the left-hand side (LHS) of R and some part of S.

Example 1:
'1' A(x,y~u)→ A(x!1,y~p),B(x!1)
//initial solution
%init : 10*A(x,y~u)
%init : 10*A(x!1,y~u),C(x!1)
%init : 10*A(x,y~p)

Here R has 10 injections. A(x,y~u) has no injections to A(x!1,y~u) because the link state is incompatible, A(x,y~u) has no injections to A(x,y~p), because the internal states are incompatible.

 The Application of the rule is a replacement injection from LHS to RHS of the rule. In the Example 1, after application of the rule '1' we will have 1*A(x!1,y~p),B(x!1), 9*A(x,y~u), 10*A(x!1,y~u),C(x!1), 10*A(x,y~p)

Each rule has the actions. Here is the list of the example rules, describing the possible actions:
'1' → a(x)
'2' b(x)→
'3' a(x),b(y) → a(x!1),b(y!1)
'4' a(x!1),b(y!1) → a(x),b(y)
'5' a(x~u) → a(x~p)
'6' a(x,y),b() → b(), a(x,y)
'7'a(x!1),b(z!1) → b(z!1), a(x!1)

The meanings of the actions are the following:
'1' has the action “add a(x)”
'2' has the action “delete b(x)”
'3' has the action “bound a.x and b.y”
'4' has the action “break a.x and b.y”
'5' has the action “modify a.x”
'6' has the actions “delete a(x,y)”, “delete b()”, “add a(x,y)”, “add b()”
'7' has the actions “break a.x and b.z”,“delete a(x,y)”, “delete b(z)”, “add a(x,y)”, “add b(z)”. “bound a.x and b.z”

The Automorphism number of the rule is the LHS symmetries number.

For example (Example 2),
the FirstExampleRule: A(x),A(x) → B(x) @0.01 has the automorphism number 2;
the SecondExampleRule: A(x,y),A(x),A(x),A(x,y) → A(x),A(x) @2.0 has the automorphism number 2*2 = 4.

Here @0.01 and @2.0 are the rule rates for FirstExampleRule and SecondExampleRule respectively.

The Activity of the rule is the number of injections from the rule to the solution multiplied by the rule rate and divided by the automorphism number.

In Example 2,
the FirstExampleRule has the activity equal to numberOfInjections*0.01/2;
the SecondExampleRule has the activity equal to numberOfInjections*2/4.

Each moment only one rule may have the infinity rate.

The Interface of the agent type is a set of sites which belongs to all agents of this type.
Therefore, the following input data
'incorrect' B(x)→ A(x)
%init : A(x,y)
%init : A(x)
is incorrect because
- the “incorrect” rule has the add action which adds an agent with incomplete interface
- the second initial condition contains an agent with incomplete interface.

The Simulation is a process of the rules application to the initial solution. On each step we summarize all activities of the rules, choose the rule according to the rate of its activity, and apply this rule to the solution. If some rule has infinity rate we choose it.