Abstracting

1. Introduction

We need Abstracting for SubViews.

2. Definitions

Agent – the substance which has the following properties:
  - Unique ID
  - Name - «nameId»;(type, for example: A,B,C )
  - Site map or set of maps: siteMap;

Site – agent’s site; contains:
  - LinkState
  - InternalState
  - has the name property: «nameId»

Linked Site (LinkedSite) – the site to which the given site is connected (in the example LinkedSite for site «1» is site «2»).

1
2

Given Site

Linked Site
Considered relatively to the Given Site

Picture 1

Link State (LinkState) – is located on each site and contains the information about the connection with some LinkedSite . For better understanding of what the Site and its LinkState are, it is more preferable considering them as a whole. LinkState can store the information about one LinkSite only. Additionally, the LinkState stores the information about the connection type – “StatusLinkRank”.

Examples of LinkState:
- A(x) - link rank of site "x" does "FREE"
- A(x!1),B(y!1) - link rank of site "x" does "BOUND"
- A(x!_) - link rank of site "x" does "SEMI_LINK" (only for rules)
- A(x?) - link rank of site "x" does "BOUND_OR_FREE" (only for rules)

Internal State (InternalState) - is located on every Site and contains the information about the internal site state along with:
  - «nameId»(type, for example «p», «u»)
There are some cases when the Site does not have any InternalState, , then the specific constant is assigned to the «NameId» field.

Abstracting –the result of transforming all the standard components (Agent, Site, …) into abstract ones. At such transformation the LinkState loses the link to the LinkedSite, but remembers the type of the LinkedSite and the type of the parent agent for the LinkedSite.

A
B
A
B

x
y
x
y

y.B
x.A
abstracting
before

after

site

Abstract site

Abstract Link State

Picture 2

Let us further name all the above mentioned objects that have passed the abstracting process as Abstract.

1. Abstract link State (ALinkState) – similar to LinkState, but contains only the site type the the type of parent agent instead of the link:
  1. «linkedSiteNameId» - type of the LinkedSite
  2. «linkAgentNameId» - type of the Agent that contains the LinkedSite.

Abstract Site (ASite) – similar to “Site”,but contains “ALinkState” instead of LinkState.

Abstract Agent (AAgent) – similar to “Agent”, contains “ASite” instead of “SiteMap”.

3. Algorithm

Abstraction process is described in the Sample section.

// Agent abstraction
createAbstractAgent(Agent GivenAgent)
    1. Create the Abstract Agent: aAgent
    2. Assign a name to the aAgent: GivenAgent.NameId
    3. For (site : GivenAgent.SitesMap)
    1. create the AbstractSite
    2. add the AbstractSite to the aAgent
    1. Return aAgent;

// Site abstraction
createAbstractSite(Site givenSite)
    1. Create the Abstract Site object: aSite
    2. Assign the nameId and the internalState for the “Site; values equal to the GivenSite values.
    3. Create the Abstract Link State object: aLinkState
    4. Add aLinkState to the aSite
    5. Assign the statusLinkRank for the aLinkState, which is equal to the statusLinkRank of the GivenSite.LinkState.
    6. Fill the information about linkSiteNameId and linkAgentNameId in the aLinkState field according to the Abstract Link State definition.
    7. Return aSite.
4. Examples

'AxBx' A(x),B(x) -> A(x!1),B(x!1) @ 1.0
'AyCy' A(y),C(y) -> A(y!1),C(y!1) @ 1.0
'Ax_Cxy_' A(x!_),C(x,y!_) -> A(x!1),C(x!1,y!_) @ 1.0

# Initial Conditions:
%init: 1 * (A(x,y),B(x),C(x,y))

There is no difference in building abstractions for the Solution or Rules, etc. Below you can see the result of LocalViews building for the model described above.

  1. Abstracting Rules and Solution:

A

B

A

B

AxBx

x
x
x
x

x.B
x.A

A

C

A

C

AyCy

y
y
y
y

y.C
y.A

A

C

A

C

Ax_Cxy_

x
x
x
x

x.C
x.A

y

BOUND

y

BOUND

BOUND

Initial Solution:

A

B

x
x

C

y

y

x