SubViews

1. Introduction

We need SubViews for RuleCompression, ContactMap, etc.

2. Definitions

1. class Sub View – the subset Agent's sites. C(A) — set of all class Sub View agent of type A.
We use BDD (Binary decision diagram) for storage subviews of agent.

2. Cov1 (backward closure). If a rule tests a site a in an agent A and
modifies a site b in the same agent, any class in C(A) that contains
b must also contain a.
3. Cov2 (relay). If a rule tests a site a in an agent A, and A is connected
by some path through a site b to an agent that is modified, any
class in C(A) that contains b must also contain a.

Classes creation is proceeded according to the following rules: С
First, we create classSubView for each site.

Transformation1. If the R rule changes the ”а”, ”b” sites, then we merge two classSubView that contain ”а”, ”b”.

- Transformation 2. If the R rule changes the “a” site and tests the “b” site, then we add the classSubView containing the “b” to the classSubView containing the “a”.
- Remove any class that would be included in another one.

4. Sub View contains the classSubView and for an agent — the set of all possible states and sites from this classSubView that can be obtained within this model.

3. Input Data

Kappa model – the file with the system model that contains the set of “Rules” and represents the Initial Solution.
4. Goal

The goal is to build the SubViews using the input data.
5. Solution

1. First, we form the set of classSubViews: we take n number of sites of our agent and divide it to n subsets (one element after another).
2. Then we transform these subsets (according to the rules described in the Definitions section).
3. The process is aimed to comply with the “Rules” until there will be nothing added to the “Solution” after passing all the rules.
6. Algorithm

For the obtained classSubView, fill the SubView.

1. Set shouldDo to TRUE
2. While( shouldDo ) do
  - a). shoulDo = false
  - b). for( r : Rule )
- find all the injections for this rule
- apply the rule for all possible injections’ combinations, using exhaustive search
- add the result applying the rule to the SubViewStorage
- if ( something new is added to the SubViewStorage) shouldDo = true

7. Examples
'AxBx' A(x),B(x) -> A(x!1),B(x!1) @ 1.0
'AyCy' A(y),C(y) -> A(y!1),C(y!1) @ 1.0
'Ax_Cxy_' A(x!_),C(x,y!_) -> A(x!1),C(x!1,y!_) @ 1.0

# Initial Conditions:
%init: 1 * (A(x,y),B(x),C(x,y))

1. Rule 'AxBx' - changes two sites.
2. Rule 'AyCy' - changes two sites.
3. Rule 'Ax_Cxy_' - changes two sites and tests one.

Filling the classSubView in according to rules described in the Definitions section, we get five different classSubViews:

Agent: A ; Sites: x
Agent: A ; Sites: y
Agent: B ; Sites: x
Agent: C ; Sites: x,y
Agent: C ; Sites: y <------------------------- removed, because it is included in “Agent: C ; Sites: x,y”

  1. Applying Rule 1: 'AxBx' , and the SubViewStorage now looks like it showed on the picture below:

A
x
A
y
B
x
C
x
y
A
x
x.B
B
x
x.A

  1. Applying Rule 1: ' AyCy' , and the SubViewStoragenow looks like it showed on the picture below:

A
x
A
y
B
x
C
x
y
A
x
x.B
B
x
x.A
A
y
y.C
C
x
y
y.A

Applying Rule 1: ' Ax_Cxy_', and the SubViewStorage now looks like it showed on the picture below:

A
x
A
y
B
x
C
x
y
A
x
x.B
B
x
x.A
A
y
y.C
C
x
y
y.A
A
x
x.C
C
x
y
y.A
x.A

The end.

Then we have to fill these classSubView in in order to get SubViews:

Agent: A ; Sites: x
- A(x)
- A(x!B.x)
- A(x!C.x)

Agent: A ; Sites: y
- A(y)
- A(y!C.y)

Agent: B ; Sites: x
- B(x)
- B(x!A.x)

Agent: C ; Sites: x,y
- C(x,y)
- C(x,y!A.y)
- C(x!A.x,y!A.y)
8. Flowchart

Start

Abstract Rules

Abstract Solution

ShouldDo = true

ShouldDo

r : Rules

End
+

newData = apply rule
ShouldDo = false

addNewDataToSolution(newData)

+
-
-
ShouldDo = true

Chart 1

Start applying the rule

All Injections = create All Injections

injections! = null
Injections = get first injection

newData = new empty list

Return newData
-

Add current application to newData

injections = generate next injections (all injections)

Chart 2

9. Remarks

The algorithm Apply Rule has some imperfections.

r : Rule's
newData = apply rule

addNewDataToSolution(newData)

+
-
ShouldDo = true

(*)

It is obvious that after applying the block (*) of the general algorithm, we will have to perform the search of all possible injections next time we start the process (if ShouldDo = true). Clearly, one of the injections should be applied to the new part.

Injections set
rule

Injections set

New inj. set
rule

Old injections

new injection

Picture 3

The following optimization is necessary:

  - Divide all the substances from the Solution into three groups; the division is performed for each substance according to a specific rule.

I group — old injection
II group – current injection
III group – new injections

  - Then, during the process of forming the set of injections, determine which types of agents are present in it,. In case, when all the agents belong to the I group, form another set of injections.
  - After applying the rule, assign type III to all the substances.
  - After executing block (*),perform the following action:
Add II group to I group
Clear II group
Add III group to II group
Clear III group

Thereby, we do not have to apply the rule for the processed set of injections iteratively.