Rule compression
# Introduction
The rules in the Kappa model may contain some duplicated or unused information. Sometimes we can replace some rule by the shorter one, or even reduce a set of rules to just one rule.

Example:
A(k!1, n~p), B(l!1) -> A(k!1, n~q), B(l!1)
During the whole simulation process, for any type A agent with the site k, if the site k is connected to something, then it is connected to the site l of the type B agent. So this rule can be shortened to:
A(k!_, n~p) -> A(k!_, n~q)

Let us find out how to do this in the general case.
# Definitions
The Root is a fixed agent in the connected component on the left-hand side of the fixed rule. An agent can be chosen as a root in 2 cases:
1. The current rule does not modify the component this agent belongs to.
2. The current rule modifies this agent directly.

Example:
A(x, y!1), B(u!1, v), C(z), H(n, m) → A(x, y!1), B(u!1, v!2), C(z!2), H(n, m)
The agent A cannot be a root, because this rule modifies the component AB, but A stays untouched.
The agent B can be a root, because this rule modifies both the component AB and the agent B.the agent C can be a root by the same reason.
The agent H can be a root as well, because its component (that contains of the agent H only) stays unaltered after the rule application.

The Rooted Connected Component is a component with the chosen root. More formally, we can define the Rooted Connected Component as a pair (this component, an agent chosen as a root).

In the example above we have:
A(x, y!1), B(u!1, v) can be rooted in the single manner: we can choose only the agent B as a root. So, the Rooted Connected Component corresponding to AB is A(x, y!1), B (u!1, v) or, in the other words, a pair ( (A(x, y!1), B(u!1, v)) , 'B' ).

The Rooted Rule is a rule such that each component from its left-hand side is rooted (for each component we choose a root and fix it).

In the example above we have:
A(x, y!1), B(u!1, v), C(z), H(n, m) → A(x, y!1), B(u!1, v!2), C(z!2), H(n, m)
This is the rooted version of the old rule: for each of three connected components of the left-hand side we chose a root marked with the bold letter.

The Reachable Species for the rule R ([R]) is a set of pairs (Si, F), where
Si is a subview that can take part in the application of R;
F is a trivial mapping: Si → left hand side of R; where each agent of Si is mapped to the corresponding agent from the left-hand side.

Example:
Look at the rule R from the previous example. If we have, for instance, C(z~p, j, l!0), K(p!0) in a solution, then the subview “z.C, which has an internal state p” (information about the site z) will be contained in [R].
# Input Data
The input data is a set of the rules.
# Output Data
The output data is an equivalent reduced set of the rules.
# Goal
Our goal is to learn how to perform the following actions with the set of rules:
1. Qualitative compression. We try to make each rule shorter.
2. Quantitative compression. We try to reduce the set of rules to the single rule, so that the system with the new set of rules is equivalent to the old one, i.e., the reachable species for the group are the same as the reachable species for the single rule.
# Solution
The main idea is to collect the most compressed information about the rules' actions and to build a new set of rules using this information.
# Algorithm
## Preparation. Creation of rules' classes
Before we can start changing a rule we should gather information about actions this rule performs in order to be able to check whether the new system is be equivalent to the old one or not. First of all, we suppose that the rules contain no cyclic patterns, neither in the left-hand side, nor in the right-hand side. Let us mark each agent of the rooted component RC from the left-hand side of the rule:
1. G is a root for RC.
2. For each agent we can find a pathway from G to the agent. The path contains connections as edges and agents as vertexes. .
3. The path is uniquely defined as the sites sequence. This is a sequence of the edges' ends.
4. Each site can be defined as a triplet (G, path-to-agent, site-name)
Consequently, each action can be described as:
ADD(G, path1, name1);
DELETE(G, path1, name1);
BREAK(G, path1, name1);
BOUND((G, path1, name1), (G, path2, name2));
MODIFY(G, path1, name1);
TEST(G, path1, name1) – if the component is just tested.

Let us call all these objects the ActionInfo. For any rule we can find the set of it's ActionInfo. Let us call this set the ActionsInfo.
## Algorithm
1. Create a list of rooted rules using the given list of rules. For each rule we create all possible rooted rules.
2. For each rooted rule R we create a set of actions descriptions denoted as AI(R).
3. Group the rules that perform exactly the same actions.
4. For each rule R we calculate [R] as the intersection of A(R) and B(R), where
A(R) is model-independent and contains the subviews that describe the left-hand side of R.
B(R) contains the reachable subviews with the same agent type as for one of the roots. We build B(R) on the process of algorithm.

1. Compression.
    1. Quantitative mode
We run down all the rules and try to shrink each of them (R). We do it step by step: remove the internal state test and check equivalence of the old rule and the new rule Rone, remove link state test and so on . If [R] = [Rone], then R can be replaced with Rone.

    1. Qualitative mode
In this part, we can try to shrink each group of rules. For each rule we create Rgroup with the common part of the rules Ri from the group. If [Rgroup] = union [Ri], then the whole group can be replaced with Rgroup . Otherwise, subdivide the group to several groups with the larger common part.
# Flowchart

Compression mode

For each rule R
create rule Rone
[R] = [Rone]
Yes
Yes
Replace R by Rone
No

Mark R as handled

For each rooted rule R
calculate AI(R) and [R]
Create set of rooted rules
Quantitative
Qualitative
No
Group rules
by AI(R)
There is
unhandled
rule R

Create rule Rgroup
for group G
There is
unhandled
group G
Yes

STOP

∪[Ri] = [Rgroup]
where Ri from G
No
Yes
Replace all Ri
by Rgroup

Mark G as handled

No
Divide G